## Slide 1: Dania Beach Downtown Asset Management and Assessment
/
Project Team

## Slide 2: Limits of Study
Downtown Area
FEC Tracks to NE/SE 1st Ave, including both sides of Road
Stirling Rd to Griffin Rd.

## Slide 3: Goals of Study
Identify City assets on the surface
Assess condition of those assets
Collect information on other assets
Identify maintenance needs
Identify areas for improvements

## Slide 4
Created an on-line tool from phones with mobile RTK-GPS
Notes: Data Collection system, is custom built for this, all data collection is done with RTK ( real-time Kinematic) GPS with sub-cm accuracy utilizing the FDOT Network Linked to completely interactive field data input is joelakner.com/test

## Slide 5: What Data was gathered
Roadways,
Curb locations,
Sidewalk limits,
Street Signs,
Water Main (as defined by valve box locations),
Sewer Lines (as defined by manhole locations),
Service laterals and meters
Storm water catch basins,
Green Infrastructure,
Location of poles, street lights, and traffic devices

## Slide 6: Assessment Rating System
Good
  No repair needed for 3 to 5 years
  This time could be extended after more data over time is collected.
Fair
  Repair could be needed in 1 to 3 years
Poor
  Repaired needed this year

## Slide 7: Mapping Assets

## Slide 8: Assets
Asset | Number |  | Asset | Number | 
Backflow DW | 35 |  | Manhole Elect | 12 | 
Bike Lock | 5 |  | Manhole SS | 69 | 
Bus Bench | 6 |  | Meter DW | 106 | 
Catch Basin SW | 57 |  | Observation Well | 5 | 
Cleanout SS | 26 |  | Pole Elect | 105 | 
Control Box | 10 |  | Pole W\ Transformer | 16 | 
Crosswalk Signal | 20 |  | Pull Box | 97 | 
Curb | 87 |  | Reclaimed Water Box | 10 | 
Curb Inlet | 20 |  | Sidewalk/Curb | 289 | 
Do Not Enter | 10 |  | Sign | 68 | 
Fire Zone | 1 |  | Stop Light Pole | 12 | 
Riser | 4 |  | Stop Sign | 24 | 
One Way | 2 |  | Street Light | 42 | 
Bollard | 1 |  | Swale | 5 | 
Electric Meter | 1 |  | Transformer | 1 | 
Fiber Optic Riser | 8 |  | Trash Can City | 9 | 
Fire Hydrant | 26 |  | Valve DW | 77 | 
Fire Sprinkler | 1 |  | Valve Gas | 11 | 
Irrigation Control | 8 |  | Yield | 1 | 

## Slide 9: Condition
Red Dots need work

## Slide 17: Process
Determine Goals & Objectives
Inventory of Assets
System Review & Assessment
AMP
Implementation
Quality Assurance
Proformance Feedback

## Slide 18: Summary of Asset Condition
Category | Frequency | Percent
Good | 815 | 63%
Fair | 399 | 31%
Poor | 73 | 6%
Assessed Points – City of Dania Beach | 1287 | 

## Slide 19: Cost = $460,000
Some of this could be CDBG funds
CRA Funds
Storm water Funds
General Maintenance dollars

## Slide 20
Blue= new sidewalks
White = new curbs
Green = Bioswale
Hatching = Pavers
Orange = crosswalk

## Slide 23: Improvements
$450,000 in maintenance needs today
Part of Oasis 9 = $80,000
Curbing - $60,000
Sidewalk upgrades - $70,000
Pavement - $75,000
Storm water - $30,000
Water Main - $ 35,000

## Slide 24: Experiment – FAU: Mobile Mapping for the future

## Slide 25: Questions?